## Slide 1
Low-Latency EOG-Based Early Intent Detection for Eye Movements
Biomedical Signal Processing & Machine Learning
Technical Project Presentation

## Slide 2
Why Detect Eye Movement Before It Finishes?
The Latency Problem
Optical tracking: camera delay + computation + waiting for saccade completion = 300+ ms
Conventional systems register command only after eye settles (200–400 ms)
The EOG Advantage
Detect saccade onset electrically, not optically
Predict direction within 20–100 ms of movement start
Immune to occlusion, lighting, and head movement

## Slide 3
How Does EOG Detect Eye Movement?
The Eye as an Electrical Dipole
Cornea: positive pole (~0.4–1.0 mV)
Retina: negative pole
Eye rotation → dipole rotates → electrode potentials change
Voltage–Angle Relationship
For small angles: — voltage is approximately proportional to eye rotation.

## Slide 4
Dataset & 16-Channel EOG Configuration
Dataset Overview
14
Subjects
S1–S14
4032
Total Trials
288 per subject
36
Target Directions
12° eccentricity
256
Hz Sampling
16 EOG channels
Why 16 Channels?
Standard 2-Channel EOG
Poor oblique-angle resolution, vulnerable to EMG artifacts
16-Channel Isotropic Montage
Full 2D voltage-gradient map, 360° directional coverage

## Slide 5
Signal Processing Pipeline
Strict Causality: No future samples used — valid for real-time deployment.
Raw EOG
16 channels acquired
Baseline Centering
First 25 samples ≈ 97.6 ms
High-Pass Filter
0.1 Hz causal drift suppression
Z-Score Norm
Training-fold statistics only
Onset Detection
→ Window → Features → Class
Baseline correction:

## Slide 6
Finding Saccade Onset
Six-Step Detection
1
Select 4 highest-variance channels
2
Spatial RMS aggregation
3
3-sample causal smoothing
4
Forward derivative calculation
5
MAD adaptive threshold
6
3-sample persistence check
MAD Threshold Formula
Early Window Sizes at 256 Hz
Window | Samples
20 ms | 6 samples
100 ms | 26 samples
200 ms | 52 samples
Target cue onset ≠ saccade onset — 150–250 ms neural delay separates them.

## Slide 7
Feature Engineering: 210 Dimensions
Per-Channel Features × 16
Amplitude / Statistical
Voltage displacement, mean, std dev, min, max, peak-to-peak
Temporal / Derivative
Regression slope, mean derivative, max positive/negative derivative
Energy / Integral
Derivative energy, signal energy, area under curve
Spatial Features × 2
Normalized index of channel with maximum voltage shift
Magnitude of maximum shift
16 × 13 + 2 = 210
Total feature dimensions per trial window

## Slide 8
Can Direction Be Predicted from 20 ms?
8-Class Octant Accuracy vs. Window Duration
Classification Schemes
Scheme | Chance
4-class cardinal | 25.0%
8-class octant | 12.5%
36-class fine radial | 2.78%
Models
L2-regularized logistic regression
One-vs-rest linear SVM
Key Finding: Directional information is present in the first 20 ms. Errors concentrate in adjacent octants.

## Slide 9
Software Architecture & Verification
System Stack
Frontend
React + TypeScript
Backend
Python FastAPI
Modules
Overview, Dataset Explorer, Signal Processing
Early Window Lab, Experiments, Data Quality
Methodology, About / Milestones
Testing & Verification
27
pytest Tests
100% pass rate
5.22s
Execution Time
Full test suite
Coverage
API, dataset loader, feature extractor
Onset detector, preprocessor
Trial segmenter, window generator

## Slide 10
Conclusion & Future Work
Key Findings
1
EOG encodes directional intent within the earliest part of a saccade
2
8-class decoding reaches 44.2% accuracy at 20 ms window
3
Accuracy scales to 82.4% at 200 ms — all causally processed
Future Directions
1D-TCN + ST-CNN
Causal dilated residuals & spatial modeling
Continuous Angular Regression
0°–360° prediction
Cross-Subject Adaptation
DANN, Riemannian alignment
Wearable Configuration
4–6 channel electrode setup
Goal: Reduce latency while preserving causal, real-time operation.